## Slide 1
1
Group Members:
Anurag Upadhyaya(077BEL007)
Arjun Oli (077BEL010)
Pratik Panuhar (077BEL029)
Rohan Simkhada (077BEL035)
Project Supervisor:
Assoc Prof. Anil Panjiyar
Er. Rabin Poudel
Onboard chargers for EVs using Dual Active Bridge and Totem Pole PFC
April 2025

## Slide 2
Table of Contents
Introduction
Project Objectives
Methodology
Results and Discussions
Conclusion
I
III
VI
VII
VIII
3
7
26
35
44
Page
IV
System Overview
9
II
Problem Statement
5
2
Literature review
V
15

## Slide 3
Introduction
Chapter I
Onboard chargers for EVs using Dual Active Bridge and Totem Pole PFC
3

## Slide 4
  Electric Vehicles (EVs) are gaining popularity due to environmental concerns. Onboard charging systems are crucial for EV adoption and convenience. Our project focuses on developing an efficient onboard charging system.
Introduction
I
4

## Slide 5
Problem Statement
Chapter II
Onboard chargers for EVs using Dual Active Bridge and Totem Pole PFC
5

## Slide 6
Problem Statement
II
Compact, effective, and reasonably priced on-board chargers are becoming more and more in demand as EVs become more widely used. Conventional isolated DC-DC converters can be large and inefficient, and boost-based PFC topologies suffer from higher conduction losses because of input bridge diodes.
6

## Slide 7
Project Objectives
Chapter III
Onboard chargers for EVs using Dual Active Bridge and Totem Pole PFC
7

## Slide 8
Project Objectives
III
1. To Facilitate Efficient Onboard Charging
Develop an efficient onboard charging system for EVs, optimizing charging speed and minimizing energy loss.
2. To Implement Totem Pole PFC
Implement and analyze Totem Pole Power Factor Correction (PFC) for AC-DC conversion, improving power efficiency and reducing harmonics.
3. To Design Dual Active Bridge Converter
Design a Dual Active Bridge (DAB) converter for DC-DC conversion.
8

## Slide 9
System Overview
Chapter IV
Onboard chargers for EVs using Dual Active Bridge and Totem Pole PFC
9

## Slide 10
Battery Pack
Stores energy for powering the electric motor.
System Overview
IV
Filters
Reduce electromagnetic interference and noise in the system.
Charging System
Manages the charging process, converting AC power to DC and regulating battery charging.
Electric Motor
Converts electrical energy into mechanical energy to propel the vehicle.
Electric Vehicle Control Unit
Manages overall vehicle operation, including powertrain control, charging, and safety systems.
AC-DC Converter
Converts grid AC power to DC power for battery charging.
Thermal Management System
Regulates the temperature of the battery pack and other components to ensure optimal performance and safety.
10

## Slide 11
System Overview
IV
11

## Slide 12
System Overview
IV
On board charging
  A bridge between Electrical Vehicle Supply Equipment(EVSE) and the battery.
  Converts alternating current available in the grid to direct current which charges the battery in the vehicle.
  Critical component in electric vehicles (EVs), enabling them to charge their batteries from standard electrical outlets or dedicated charging stations.
12

## Slide 13
System Overview
IV
AC-DC Conversion
  Most electrical power from the grid is supplied as Alternating Current (AC).
  Batteries and many electronic devices require Direct Current (DC) to operate.
  AC-DC converters bridge this gap by transforming AC into usable DC power.
  Essential for applications like:
    Electric vehicle charging
    Power supplies for electronics
    Renewable energy systems
13

## Slide 14
System Overview
IV
DC-DC Conversion
  Convert the AC from the AC-DC phase and supplies the power to the battery system.
  Various circuits maybe chosen for this purpose such as LLC resonant converter, Phase shifted full bridge converter and Dual Active Bridge converter
  Essential requirement for this phase is to provide high efficiency, voltage stability and galvanic isolation.
14

## Slide 15
Literature Review
Chapter V
Onboard chargers for EVs using Dual Active Bridge and Totem Pole PFC
15

## Slide 16
Literature Review: AC-DC Conversion
IV
Controlled Bridge Rectifier
16
  Converts AC to controlled DC using thyristors.
  Output regulated by adjusting firing angle.
  Types: half-controlled and fully-controlled.
  Used in motor drives, chargers, and power supplies.
  Offers variable DC output and high efficiency.

## Slide 17
Literature Review: AC-DC Conversion
IV
Controlled Bridge Rectifier
17
Major Disadvantage:
Pulsating DC Voltage
Pulsating DC causes inefficient charging, battery overheating, reduced battery life, and can damage sensitive battery chemistries.

## Slide 18
System Overview: AC-DC Conversion
IV
18
Controlled Bridge Rectifier with Capacitor
  Capacitor smooths pulsating DC.
  Provides steady output voltage.
  Reduces ripple and heating.
  Increases charging efficiency.
  Lowers electromagnetic interference.

## Slide 19
System Overview: AC-DC Conversion
IV
19
Controlled Bridge Rectifier with Capacitor
Major disadvantage: Capacitor-filtered controlled rectifiers have a poor power factor, especially at light loads.
Why: Current becomes highly peaky and out of phase with voltage, causing inefficient power use and stressing the AC supply.

## Slide 20
System Overview: AC-DC Conversion
IV
20
Totem Pole Power Factor Correction
  Active switches in one leg, diodes in the other.
  High efficiency, low losses.
  Near-unity power factor.
  Compact with fewer components.
  Fast response to load changes.

## Slide 21
System Overview: AC-DC Conversion
IV
21
Totem Pole Power Factor Correction
Totem Pole PFC improves power factor by shaping the input current to closely match the input voltage. The waveforms show minimal phase difference and distortion, indicating high power factor and efficient AC-DC conversion.

## Slide 22
System Overview: AC-DC Conversion
IV
22
Totem Pole PFC: Operating Modes
Zero State Operation
In this state, the inductor is charged and the capacitor powers the load

## Slide 23
System Overview: AC-DC Conversion
IV
23
Totem Pole PFC: Operating Modes
Active State Operation
In this state, the Capacitor is charged and the inductor powers the load

## Slide 24
System Overview: AC-DC Conversion
IV
24
Dual Active Bridge Converter
Source: www.alife-robotics.co.jp
Primary Side: The primary bridge converts the input DC voltage (from the AC-DC conversion stage) into
a high-frequency AC voltage.
Transformer: The high-frequency AC voltage is transferred through the transformer, which adjusts the voltage level based on the turns ratio.
Secondary side: The secondary bridge rectifies the high-frequency AC voltage back into DC voltage, suitable for charging the EV battery.
Phase Shift Strategies: In Dual Active Bridge (DAB) converters, power transfer is controlled by
adjusting the phase shifts between voltage waveforms

## Slide 25
System Overview: AC-DC Conversion
IV
25
Dual Active Bridge Converter
Source: www.researchgate.net
Various control strategy are used for DAB and we have chosen single phase shift for its low complexity
S1,S4 are triggered at first, then at some angle phi S5 is triggered. This is the single phase shift control strategy.

## Slide 26
Methodology
Chapter VI
Onboard chargers for EVs using Dual Active Bridge and Totem Pole PFC
26

## Slide 27
Methodology
V
27
Fig: SIMULINK Model for Totem Pole PFC Circuit
We have used MATLAB Simulink for our project.

## Slide 28
Methodology
V
28
Fig: SIMULINK Model for Totem Pole PFC Circuit control

## Slide 29
Methodology
V
29
Calculation of individual parameter:
For totem pole pfc:
•Vin = 85–265 V
•Vout = 400 V
• Pout = 2–5 kW
•Fline = 50 Hz
•Fsw = 40 kHz
•Iripple = 0.3
•Vripple = 0.01
•IL = 2500 0.95×85 = 30.98
•Ipeak = IL × 1.30 = 30.98 × 1.3 = 40.27 A
• L = Vout/ 4×fsw×Iripple = 400 /4×40×10^3×0.3×43.78 = 1.903 × 10^-4 = 190.3 µH
•Cout = Pout / Vout 4π× Fline × Vripple = 2500 / 400 4Π × 400 × 0.01 × 50 = 2486.71 µF

## Slide 30
30
Fig: SIMULINK Model for DAB Circuit

## Slide 31
Methodology
V
31
Po = Vi² · dΦ / Xl(1 – Φ / Π)
Po = 2500
Vi = 400
Put L = 0.3 × 10^-6 H
d = Vo / nVi
n = ½
For Vo = 200 V
Vi = 400 V
d = 2 × 200 / 400
d = 1
2500 = 400² / 2Π × f × 0.3 × 10^-6 · Φ(1 – Φ / Π)
Also, f = 500 kHz = 500 × 10³
2500 = 169765.2726 Φ(1 – Φ / Π)
0.0463 = ΠΦ – Φ²
Φ² – ΠΦ + 0.0463 = 0
Φ = 3.13 ,0.0148(in radian)
Φ =179.33, 0.85(in degree)
Since,-90<phi<90
So,
Φ=0.85
For dab converters we have used two model where in the first model we have provided a manual phase shift in pulse generator

## Slide 32
Methodology
V
32
Here we generate required phase shift from the difference between output voltage and constant value

## Slide 33
Methodology
V
33
Integration of AC/DC and DC/DC phase:
Note that above is for a constant phase shift

## Slide 34
Methodology
V
34
Design of Filter and system parameters:
•We tried various values of L and C values to smooth out the circuit and finally settled for the following system parameter:
•Input Voltage=230V rms (AC)
•Output Voltage=200V DC

## Slide 35
Result and Discussion:
Chapter VII
Onboard chargers for EVs using Dual Active Bridge and Totem Pole PFC
35

## Slide 36
Result and Discussion:
VI
36
Output for individual circuits:
For dual active bridge converter with manual phase shift provided:
We can see a constant 200V which was obtained as desired

## Slide 37
Result and Discussion:
VI
37
Output for individual circuits:
For totem pole pfc circuit:
We can see a voltage level with ripple oscillating near 400V which was the desired voltage level

## Slide 38
Result and Discussion:
VI
38
For the voltage output at the dual active bridge converter side:
Output for combined circuits:
Though we receive a constant voltage of 198.2 at the end of our simulation time which was T=60s which is efficient at 98% but we can see that this is for a limited simulation time and at higher simulation voltage decrease considerably.

## Slide 39
Result and Discussion:
VI
39
For the voltage output at the toem pole pfc circuit side:
Output for combined circuits:
We receive a constant 400V at the totem pole side and this value does not drop with time as it is maintained with the help of a closed loop control system which was not the case at the dab side so to maintain constant voltage we use a closed loop system at dab side too.

## Slide 40
Result and Discussion:
VI
40
For the voltage output at the dual active bridge converter side:
Output for individual circuit closed loop DAB:
Voltage is maintained at around 200V which is as desired.

## Slide 41
Result and Discussion:
VI
41
Integration of DAB and Totem pole circuit with phase from the difference between output
voltage and constant value:
We have obtained following output with this type of circuit, one of the advantage of using this is that the voltage level does not drop even at the higher simulation as it did in the open loop model and voltage is maintained constant at value around 201 Volts. This model was also found be compatible with higher switching frequencies and had flexible switching option.

## Slide 42
Result and Discussion:
VI
42
Possible sources of mistake:
• Incorrect phase shift:Providing correct phase shift becomes critical in the DAB converters as if the
provided phase shift is small the power that is supplied decreases and if it is too large there can exist excessive current flow which might result in high conduction losses.
• Incorrect switching frequencies:Choosing correct switching frequencies is also essential in these
type of circuits as the incorrect switching frequencies may result in voltage instability, incorrect
core sizes and efficiency issues.Though in our project we have primarily used a 20 KHZ switching
frequency to maintain a appropriate voltage level, this might not be the case in all the designs as the
switching frequency we choose also depends upon the sophistication of the control mechanism as well.
• Incorrect selection of parameters:Though calculation of parameters holds for individual circuit
design, while integrating different circuits its necessary to reevaluate different circuit parameters
based on the output received and in course of reevaluation there is possibility of incorrect parameter
selection which may also result in the incorrect performance of the system.

## Slide 43
Result and Discussion:
VI
43
Challenges and Limitations:
Challenges:
  Managing high-frequency switching noise, which can affect system stability and EMI performance.
  Balancing efficiency and output voltage quality in both Totem Pole PFC and DAB converter designs.
Limitations:
  Results are limited to MATLAB simulation without experimental hardware validation.
  Focused on a two-stage on-board charger circuit, not exploring newer single-stage topologies.
  Some real-world effects like parasitic elements and switching losses are not fully captured.

## Slide 44
Conclusion and Recommendations:
Chapter VIII
On board chargers using totem pole pfc and dab circuit
44

## Slide 45
Conclusion:
VII
45
Conclusion:
At end of the project:
  We successfully implemented Totem Pole PFC with 400V output
  We achieved implementation of DAB converter with the output voltage 200V
  Integrated both the circuits to create on board charging circuit topology with stable voltage.
Key highlights of the project:
  Highlights the importance of use of correct phase shift for dual active bridge converter.
  Highlights direction for design of on-board charging topology and leaves room for future hardware implementation.
  Discusses various circuit topologies that can be used for design of OBC system.
  Provides direction for future research on use of switching frequencies to balance voltage level.

## Slide 46
Conclusion:
VII
46
Recommendation for further continuation of the project:
At end of the project:
  We recommend the further research to focus on single stage OBC circuit integrating both totem pole and dab in a single stage circuit.
  Implementation of hardware circuits based on current design and improvement on current design with hardware testing.
  We recommend highlighting a deeper relation between phase shift and output voltage such. ANN based calculation can be performed for phase shift calculation.

## Slide 47
References:
Chapter IX
On board chargers using totem pole pfc and dab circuit
47

## Slide 48
References
VIII
48
[1]. S. Khan, S. Sathyan, H. Sugali, and S. S. Chandra Bommagani, “Design of on-board battery
charger using interleaved bridgeless type pfc and phase shifted full bridge converter,” in 2020 IEEE
International Students’ Conference on Electrical,Electronics and Computer Science (SCEECS), 2020,
pp. 1–5.
[2] A. K. Singh, A. K. Mishra, K. K. Gupta, and T. Kim, “Comprehensive review of nonisolated bridgeless
power factor converter topologies,” IET Circuits, Devices Amp; Systems, vol. 15, pp. 197–208, 2021.
[3] E. Network, “A comparison of interleaved boost and totem-
pole pfc topologies,” EDN, 2025. [Online]. Available: https:
//www.edn.com/a-comparison-of-interleaved-boost-and-totem-pole-pfc-topologies/?fbclid=
IwY2xjawImIaVleHRuA2FlbQIxMAABHSUxXUnO5GSOGUTTPXGTOQRbuDPqmWQ3InHB4ffOxnnCKlR
aem a1Emh dB2O8x7FLmjHiWZg
[4] B. Zhao, Q. Song, W. Liu, and Y. Sun, “Overview of dual-active-bridge isolated bidirectional dc–dc
converter for high-frequency-link power-conversion system,” IEEE Transactions on Power Electronics,
vol. 29, no. 8, pp. 4091–4106, 2014.
[5] B. Kumar, A. Kumar, A. Bhat, and P. Agarwal, “Comparative study of dual active bridge isolated
dc to dc converter with single phase shift and dual phase shift control techniques,” in 2017 Recent
Developments in Control, Automation and Power Engineering, RDCAPE 2017, ser. 2017 Recent
Developments in Control, Automation and Power Engineering, RDCAPE 2017. United States:
Institute of Electrical and Electronics Engineers Inc., May 2018, pp. 453–458, publisher Copyright:
© 2017 IEEE.; 2017 Recent Developments in Control, Automation and Power Engineering, RDCAPE
2017 ; Conference date: 26-10-2017 Through 27-10-2017.
[6] W. Qiufeng, X. Yong, and Z. Xiangwen, “Research and design of control strategy for on-board charging
system in electric vehicle,” in 2017 29th Chinese Control And Decision Conference (CCDC), 2017, pp.
6901–6905.
[7] E. Firmansyah, S. Tomioka, S. Abe, M. Shoyama, and T. Ninomiya, “An interleaved totem-pole power
factor correction converter,” in Proceedings of the 15th International Power Electronics and Motion
Control Conference (EPE-PEMC), 2010, pp. 1298–1303.

## Slide 49
Thank you for
listening
Electrical Engineering Department, IOE Pulchowk
49